## Slide 1: Internet: A Brief Overview

## Slide 2: Chapter 1: introduction
our goal:
get “feel” and terminology
more depth, detail later in course
approach:
  use the Internet as the example
overview:
what’s the Internet?
what’s a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit switching, Internet structure
performance: loss, delay, throughput
protocol layers, service models
Notes: Throughout this course, we are going to learn techniques that build and use the Internet.
Let us move to the first chapter, the introduction of the Internet.
Through this chapter, you are expected to have a basic idea on how Internet works, you don’t need to know the details on how it works.
These will be given later in the course.
In particular, we are going to answer the following questions?
“What is the Internet?” How is it made up of?
What is the protocol?
How do the network elements work (edge and core)?
How to evaluate the Internet’s performance?
What are its service model and protocol layers?
To name a few.
Note: we will not cover security and history in class.

## Slide 3: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: ============
Lec 1: course basic info + Internet History
Lec 2: chap 1.1 – 1.3 (access network and PS and CS)
===========
So far any questions? (1) waitlist (2) Have you got your project partner?
Let us move to the first question. What is the Internet?
[Interaction: Could you tell me what you think of it? What is the Internet?

## Slide 4: 1.1 What is the Internet?
Internet

## Slide 5: 1.1 What is the Internet?
Internet
Notes: Geographically, to cover the whole world, it is decoupled into multiple networks.
For example….
Each network is interconnected.
If we zoom into the network in the USA
==================
Internet is big (it is a large-scale network)
Internet is connected. Different networks are interconnected. It may traverse multiple hops… (not directly connected)…

## Slide 6: 1.1 What is the Internet?
Notes: If we zoom into the network in the USA
(Geographically. Many networks…
In addition, there are many forms of networks.
For example,

## Slide 7: 1.1 What is the Internet?
AT&T
TimeWarnerCable
Sprint
Verizon
T-Mobile
Chase
…
…
…
…
Notes: In addition, there are many forms of networks.
For example,....
AT&T, TWC...
OSU, Chase... Networks provided by the companies.
T-Mobile..... Verzion
======================
If interested, look up our networks at
https://www.broadbandmap.gov

## Slide 8: What’s the Internet: “nuts and bolts” view
hosts = end systems
  running network apps
  Billions of connected computing devices
communication links
  fiber, copper, radio, ...
  transmission rate: bandwidth
Routers and switches
  packet switching: forward packets (chunks of data)
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: 8

## Slide 9: Questions on hosts, links, routers
What else are hosts?
Are they comm. Links?
  Phone-wireless AP?
  Phone-base station?
  Router-to-router?
  Router-to-server?
How to differ routers and switches from end-hosts?
  Routers: in-between
  No network apps running (only interconnection, no web/email/etc)
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: 9
Q1: What are hosts as you know?
(How to identify whether an equipment is a host?)
SmartCar, Smart-Camera, iWatch, IoT… (sensors), machines. Data centers (Google Server)?
Q2: Is the link between switcher to the router is a communication link?
(sometimes, hop)
Q3: Do the routers and switches run network apps? (e.g, web browsing?)
What is the difference between the hosts and routers??
(Internet: offers services for end-to-end (host to host). While routers and switches are used to make it happen (forward chunks of data in between)

## Slide 10: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 11: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 12: Common Access Networks
Cable network
Digital subscriber line (DSL)
Home Wi-Fi Network
Cellular (mobile) network
Ethernet
Fiber (optics network)
…
Read Chapter 1.2 for details

## Slide 13: Access network: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  < 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
  < 24 Mbps downstream transmission rate (typically < 10 Mbps)
DSL
modem
splitter
DSL access
multiplexer

## Slide 14
ISP
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office
Access network: cable network

## Slide 15
Access network: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
wireless access
point (300 Mbps)
wireless
devices
often combined
in single box

## Slide 16: Enterprise access networks (Ethernet)
typically used in companies, universities, etc.
  100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 17: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  within building (100 ft.)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G, 5G: 3G, LTE, LTE-A, 5G
to Internet
to Internet

## Slide 18: Physical media (optional)
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
coaxial cable
fiber optic cable
Wireless radio
Read chapter 1.2.2 if interested.
Notes: [Ignore “Physical media”. Please read chapter 1.2.2]
These access technologies are provided by various physical media. You can read the slides and chap1.2.2 to learn it.
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gpbs Ethernet
  Category 6: 10Gbps

## Slide 19: Physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps

## Slide 20: Physical media: coax, fiber
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 21: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  54 Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 22: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 22
Now let us move the network core.

## Slide 23: Discussion: How to transfer data?
mesh of interconnected routers
Role: send chunks of data from one host to another host
?
Notes: The core network can be regarded as a mesh of networks.
Its task is to transfer data from one host to another host. But the question is how to?
(As shown in the picture, this is one host and this is another host?)
======== Raise a discussion on how to forward data from one host to another host…=======
Hint1: it need to occupy several communication links (multiple hops…)
Hint 2: (from our laptop to google, many hops), what hops are used? How to find these hops? How to organize them?
(see the next slide)..

## Slide 24: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header
Notes: Let us first learn the key functions that should be offered in the network core.
[Routing] …
It will determine which link it will forward (1, 2 or 3)?
[Forwarding] ….
It is the real action to move the packet out.
… After forwarding, it will arrive at another router, which repeats the above two functions until it arrives at the destinations.

## Slide 25: Network core: packet-switching
Packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
Notes: The core technique is PS. It works as follows.
(1) At the hosts side, chunk of data are divided into multiple packet, each packet is sent independently (from source to dest)
It has two major properites
[1. forward hop by hop]
[2. sent at full capacity]
Why do we use PS? Internet is used for data communication
(e.g, one host wants to send some data to another hos. For example, we want to get an 10MB video from Youtube.)
Can we send 10MB in one time (physically, one packet is 10MB long)… (many factors; it is not practical (realistic): too long to be wrong (loss/error); occupy channel too long (multiplexing), phy layer (can’t support)
=============Spring’14 ==========
The core network can be regarded as a mesh of XXX.
The key technique in the core is PS.
{Q: Ask if anyone knows what is PS? …..
Later we will explain an alternative technique… CS.
Why do we use PS? Internet is used for data communication
(e.g, one host wants to send some data to another hos. For example, we want to get an 10MB video from Youtube.)
Can we send 10MB in one time (physically, one packet is 10MB long)… (many factors; it is not practical (realistic): too long to be wrong (loss/error); occupy channel too long (multiplexing), phy layer (can’t support)
Divide into multple packet, each packet is sent independently (from source to dest)
It has two major properites
[1. forward hop by hop]
[2. sent at full capacity]
 router’s role: routing, forward,

## Slide 26: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=
Notes: Note: packet are sent via access network (that is at the network edge, not in the core)
[tx delay = L/R]
[Use blackboard: tx delay is the time between arrivals of the first bit and the last bit]
(tx delay: important concept)

## Slide 27: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)
Notes: The above slide: one-hop tx delay? How about multi-hop?
It depends how PS works.
PS use store-and-forward. [DEF of store-and-forward]?
Store-and-forward: cause delay (since the previous hop must finish before the next hop)
End-to-end Delay = N * L/R (L/R is one hop delay, N Is # hops)
[Ask why? “Store-and-forward…”. What if it is run in pipeline (no store, but forward)? ]
Q: Do you have any experience with slow web page loading or video freezon?
Do you feel that your Internet access is really slow (though it claims high speed).
Of course, there are many reasons for the delay… but one reason: multiple hop… (another reason is queuing, see next slide)
[do you realize the impact of hop)

## Slide 28: Alternative core: circuit switching
end-end resources allocated to, reserved for voice “call” btw. source & dest
Example: each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks
Notes: Now let us look at another option: CS.
It builds circuits to reserve resources for an end-to-end connection.[Example: 4 circuits]
[Explain how it works] [key points: dedicated resource, no sharing]
[Q: Does it need routing? (No routing during runtime. But the initial setup can be regarded as a routing. Static routing]
[Q: Does it need forwarding? Yes]

## Slide 29: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Here are two techniques to enable CS: FDM and TDM. (FDM: frequency division multiplexing)
%%Two simple multiple access control techniques.
Let us use animation to describe their difference.
This is resource in terms of frequency and time. Assume there are four users.
[FDM] The whole frequency band is divided into four sub-bands; each user occupies one…
Anytime, the user can use the allocated frequency sub-band only.
[TDM]: In contrary, TDM divide all the time into multiple time slots.
The users can use whole frequency band, but only at the allocated time slots.
%%%
%%% Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
%%%As we will see, used in AMPS, GSM, IS-54/136

## Slide 30: Discussion: Packet switching vs. circuit switching
Q: Why packet switching is chosen by the Internet?
Notes: [Compare PS and CS] Let us compare PS and CS and see why the Internet choose PS, not CS.
The reason is PS allows more users to use network. Let us look at this example. …
Q: how many users will be supported in CS? (10)
Q: How about PS? (35 with probability > 0.9996)
[Q: How to derive it?] it can not support 10 user at the same time. So the key question, how large is n so that it will lead to more than 10 users will use the network at the same time.
[see ch1-chunyi-other.docx]
Does it mean that PS is always better?

## Slide 31: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
* Check out the online interactive exercises for more examples
Notes: [Compare PS and CS] Why the Internet choose PS, not CS.

## Slide 32: How to calculate N in the example?
Given N users, the probability that x users are active is P(N,x)
In order to afford N users, the probability that more than 11 (including 11) users are active at the same should be extremely small (e.g., < 0.1%)
Therefore,

## Slide 33: More on “how to calculate N?”
Given N, we can obtain the probability of no more than x active users at the same time
  Calculator
  Program (sum them up)
Given the maximal probability of no more than x active users at the same time, how to calculate N?
  Approach #1: program (for loop, and increment N by 1 until it meets the threshold)
  Approach #2: Approximation via central limit theorem (optional; see the hidden slides for details)

## Slide 34: More on “how to calculate N?”
Step 0: Xi: random variable, status of user i
  Xi = 1: user i is active
  Xi = 0: user i is not active
Step 1: Z = sum(Xi), another random variable
  The number of active users, given N users in total

## Slide 35
Step II: Z conforms to normal distribution
  Xi is iid (Independent and identically distributed)
  Central limit theorem
  Z conforms to normal distribution
Step III: look up the cumulative distribution function (CDF) for a normal distribution
  Given P(Z<= 10) > 99.9%
  Let us look up the standard normal distribution, we have (for simplicity)
  Then, we have and then calculate N
https://www.stat.tamu.edu/~lzhou/stat302/standardnormaltable.pdf

## Slide 36
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss (see the following slides)
  protocols needed for reliable data transfer, congestion control
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Q: is packet switching a “slam dunk winner?”
Packet switching vs circuit switching
Notes: Q: So does it mean that PS is always a winner?
Q: In what cases CS is better?
Thinks about of two examples:
Ex1: all of us in this room want to access course websites? The access time is random.
Ex2: Google needs to sync its data center in north california with the one in Europe. The whole volume might be 1000TB.
CS: is also good to guarantee QoS. It is critical to multimedia (video and voice callls). It is still used in cellular networks of offer our voice call services.
Q: Do you have any examples of PS and CS in our daily life?
[ CS: Doctor appointment; even no one comes, it stays idle;
[ PS: office hours, emergency; bank; etc …]

## Slide 37: Finally,
Let us see how to build the Internet: network of networks.
Optional. Read Chapter 1.3.3

## Slide 38: Internet structure (Optional)
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Notes: End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other

## Slide 39: Option 1: all inter-connected?
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
Notes: First option: pairwise connection
Problem: not scale

## Slide 40: Option 2: one Global ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP?
But, Customer and provider ISPs have economic agreement with single point. Global transit ISP is the bottleneck.
global ISP
Notes: Option 2: only global ISP
Drawback: single point of bottleneck; no economic competition

## Slide 41
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C
Option 2*: multiple Global ISPs?
Notes: Multiple ISPs

## Slide 42
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point

## Slide 43
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPs
ISP B
ISP A
ISP C
IXP
IXP
regional net
Option 3: Hierarchical structure
Notes: Hierarchy is introduced…
Regional ISP

## Slide 44: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network

## Slide 45: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Notes: Eventually, it is today’s Internet structure

## Slide 46: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 46
Let us move to the performance metrics for the Internet: delay, loss and throughput.

## Slide 47: Host: sends packets of data (Recap)
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=
Notes: Note: packet are sent via access network (that is at the network edge, not in the core)
[tx delay = L/R]
[Use blackboard: tx delay is the time between arrivals of the first bit and the last bit]
(tx delay: important concept)

## Slide 48: Store-and-forward: transmission delay
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)
Notes: The above slide: one-hop tx delay? How about multi-hop?
It depends how PS works.
PS use store-and-forward. [DEF of store-and-forward]?
Store-and-forward: cause delay (since the previous hop must finish before the next hop)
End-to-end Delay = N * L/R (L/R is one hop delay, N Is # hops)
[Ask why? “Store-and-forward…”. What if it is run in pipeline (no store, but forward)? ]
Q: Do you have any experience with slow web page loading or video freezon?
Do you feel that your Internet access is really slow (though it claims high speed).
Of course, there are many reasons for the delay… but one reason: multiple hop… (another reason is queuing, see next slide)
[do you realize the impact of hop)

## Slide 49: Follow-up questions
What if we have N hops?
What if we have P packets?
  Back-to-back
Notes: What if we have multiple hops?
What if the data rate is different?
L/R1 + L/R2 + L/R3….
(2) What if we have P packets?
Back-to-back???

## Slide 50: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 51: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 52: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 53
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
Four sources of packet delay
* Check out the Java applet for an interactive animation on trans vs. prop delay
dtrans and dprop
very different
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 53

## Slide 54: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 55: Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 56: Queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1
* Check online interactive animation on queuing and loss

## Slide 57: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 58: “Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org

## Slide 59: Demo in Class
1. traceroute www.google.com
2. traceroute europa.eu
What are differences you can see?
Can you see the link across the ocean?
Why?

## Slide 60: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 61: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 62: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 63: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 64: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 64

## Slide 65
protocols control sending, receiving msgs
  e.g., HTTP, Skype, TCP, IP, 802.11
Internet standards: standardize protocol specifications
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What’s the Internet: a software view
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: Let us look at the software for the Internet. How to run the Internet?
[Analog of OS: To make a computer works, you first need to have hardware. But it is not enough. OS is required to make each component work.]
Protocol defines how the Internet works.
[Mention: it is a large scale of a distributed system]
[standard for protocols]

## Slide 66
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
time
What’s a protocol?
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
TCP connection
request
3 elements: format, order of msgs, and actions
Notes: [Example of human protocols] Bob meets Alice. …He wants to know what time it is? What will he do? Likely, …
[Similarly, you want to download course files from the server…]
[emphasize the three elements: format, order of msgs, and actions
[format]To get the time, Bob has to ask what is the time?, not blah, blah, blah…
[order]: Bob should ask the time after “Hi” .. (it is weird if Bob says Hi at the end, right?)
[action]: Alice will tells 2PM after this question. (It is the action taken.)
Btw, What if Alice gives him a wrong time, for example, 3PM? Can she do that? [Pause]
Yes… It will involve trust and security and more actions defined in the protocol. Some protocols take these into account and some not.
(e.g., TCP automatic tear down; IP spoofing
[Q: do you have any human protocols?]

## Slide 67: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… in a specific order
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt
Notes: The key technique to build Internet is its protocol.
Let us first consider the human analog. We use human protocols everywhere, for example, XXX
Do you notice what? [the properties of a protocol]
To get these information, specific msg, specific order, specific action…
Let us look at network protocols ….
[Protocol definition: be slow]….
Let us elaborate these through the following example.

## Slide 68: Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 69: Internet Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Application
Transport
Network
Link
Physical
Notes: So far, we can see that the Internet was extremely complicated: Billions of hosts, millions of routers, ….
The question is how to handle such complexity?
The answer lies in layering.
(if you remember, we actually showed the following protocol layers in our first lecture).

## Slide 70: Why Layering?
Decomposed complex delivery into fundamental components
Explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
Modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to the rest of system
Notes: Let us look at the advantages of the layering. It makes the complex system simple.
Explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
=== layering: decompose the delivery into fundamental components ===
(view from Scott Shenker)
================================

## Slide 71: Analog: air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Notes: Let us use air traveling as the example to illustrate the advantage of layering, how does it help to organize structures over the Internet.
One way is to describe each action you have taken in order.
First, You purchase your ticket, check in your baggage, go to the gate, and eventually get loaded.
The airplane takes off and carries you to the destination.
After your plane lands, you will first depart the gate and claim your bags. If the trip is bad, you may complain about the flight.
It is similar to computer networking. Packets are shipped from the source to the destination, as you are carried from one place to another.
Though all the steps are complicated, there is one way to simplify it. That is “Layering”.

## Slide 72: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
Notes: [Key: Layering]
This figure divides all the functionality into layers. Each layer implements one service.
For example, the upper layer is “ticket”. It is responsible for all functionality relevant to the ticket, such as purchasing a ticket.
The next lower layers are responsible for “baggage”, gate, taking off or landing, or routing.
The layered architecture provides a well-defined part for a large and complex system.
The service in one layer is provided via the actions within this layer.
Such a service only relies on the layer below.
For example, the ticket layer never cares about the the airplane routing layer.
It only need to ensure that it can obtain the baggage service for ticketed-users.
============ benefits of layering ======
For example, changing the procedure at the gate will not change the rest system.
For example, we now follow the order of boarding group: priority, 1, 2, 3, 4, but it is OK to use the reverse order. Group 4 boards first.
Q: layering makes the system simple, but are there any downsides?
(hide information and make it perform worse. For example, if your premier access is only available in the ticket layer, there is no privilege during boarding.)
In fact: some cross-layer designs are proposed; Later, we will see the network protocols do not strictly follow the layering design. (TCP use the IP information)

## Slide 73: Layering in Internet protocol stack
Applications
… built on ...
Reliable (or unreliable) transport
… built on ...
Best-effort global packet delivery
… built on ...
Best-effort local packet delivery
… built on ...
Physical transfer of bits
Application
Transport
Network
Link
Physical
Modified based on Source: Dr. Scott Shenker (UCB): Slide 7 at The Future of Networking and the Past of Protocols
Notes: Now we look at the Internet protocol stack. There are five layers. We take a top-down approach, first covering the application layer and then to physical layer.
The app layer is distributed over multiple end systems. This protocol allows the application in one end can communicate with the app layer in another end.
Transport layer is responsible for data transfer in support of various applications.
Network layer: route from source to dest
Link: data transfer between neighbors
PHY: move each bit from one node to another.
=== layering: decompose the delivery into fundamental components ===
(view from Scott Shenker)
Applications
… built on ...
Reliable (or unreliable) transport
… built on ...
Best-effort global packet delivery
… built on ...
Best-effort local packet delivery
… built on ...
Physical transfer of bits
Application: message
Transport: segment
Network: datagram
Link: frame
Generally speaking: packet

## Slide 74: Layering in Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
Application
Transport
Network
Link
Physical
Notes: Now we look at the Internet protocol stack. There are five layers. We take a top-down approach, first covering the application layer and then to physical layer.
The app layer is distributed over multiple end systems. This protocol allows the application in one end can communicate with the app layer in another end.
Transport layer is responsible for data transfer in support of various applications.
Network layer: route from source to dest
Link: data transfer between neighbors
PHY: move each bit from one node to another.
=== layering: decompose the delivery into fundamental components ===
(view from Scott Shenker)
Applications
… built on ...
Reliable (or unreliable) transport
… built on ...
Best-effort global packet delivery
… built on ...
Best-effort local packet delivery
… built on ...
Physical transfer of bits

## Slide 75: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  Q: are they needed?
application
presentation
session
transport
network
link
physical
Notes: There are another two layers in ISO/OSI model.
[presentation]
[session]
They should be implemented in the app layer.
But they are not used in practice.

## Slide 76: Encapsulation & Decapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
Notes: Now we will how data packets are transferred up and down the protocol stack. We use this animation to explain two important concepts: encapsulation and decapsulation.
At the sender, the message is first passed from the application to the transport layer. When it arrives the transport layer, it will append additional information, which is called transport-layer header. (Ht), ….
It will be phyisically sent out.
Switch is a L2 equipment and the router is a L3 one.
It removes the L2 header and moves it to the network layer.
When it arrives at the destination, decapsulation is done in a reverse order.
Eventually, M arrives at the application layer in the destination end.
====
Application: message
Transport: segment
Network: datagram
Link: frame
Generally speaking: packet

## Slide 77: Advanced topics (optional)
If you are interested, you can download and study the following Internet tools:
Packet sniffer and analyzer
  tcpdump (command)
    > tcpdump –i en0
    > tcpdump -i en0 -c 10 -w test.cap
    > tcpdump –r test.cap
    More usage via Google “ tcpdump”
  wireshark (UI)

## Slide 78: Chapter 1: Summary
what’s the Internet?
network edge
  hosts, access network
network core
  Packet switching versus. circuit switching
performance: loss, delay, throughput
what’s a protocol?
  protocol layers, service models
You now have overview, “feel” of the Internet
  more depth, detail to follow!
Notes: 78
Chap1 overview (stop here)