## Slide 1
Network measurement tools:
Ping: round-trip time measurement
Traceroute: latency to each intermediate hop
Network protocol analyzers:
Wireshark
tcpdump & tcptrace
Network simulator/emulator
ns-3
Internet Tools In Practice

## Slide 2: Internet Tools Leveraging ICMP
ICMP used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Tools leveraging such ICMP messages
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 3: Ping: Packet Internet Groper
Leverage ICMP echo message
Sender sends ICMP_echo request
Receiver responds with ICMP_echo-reply message
Measure the round-trip-time between these two messages
Show the statistical summary of such measurements
  Include min, max, mean (& std dev) of RTT

## Slide 4: Ping implementation
ICMP over IP
It is implemented on top of IP protocol
For Ping:
  ICMP echo request: ICMP type=8, code=0
  ICMP echo reply: ICMP type=0, code=0

## Slide 5: Traceroute
Leverage ICMP error message
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 6: iPerf
Tool for measuring maximum achievable bandwidth for IP networks (Source: https://iperf.fr/)
Client and server based implementation

## Slide 7: iPerf using TCP

## Slide 8: iPerf using UDP

## Slide 9: Useful iPerf Commands
UDP and TCP:
-i n report status every n seconds
-d do bidirectional test simultaneously
-r do bidirectional test one after another

## Slide 10: Wireshark
An Internet protocol/packet analyzer (Source: https://www.wireshark.org/)
  Capture, filter and inspect the network traffic at the packet level
Arguably the best open-source network analyzer to date
  Running on Linux, Mac OS, Windows
Usage scenarios
  Debug network protocol implementations
  Learn network protocol internals
  Trouble shoot network problems by system admin
  Examine network security issues
It is NOT
  Intrusion detection system
  Not manipulate networks but measure/observe what has happened

## Slide 11: How Wireshark Works?
Data capturing/inspecting program that “understands” the structure of different network protocols
  Parse and display different fields, along with their meanings
  Use pcap to capture packets
Let us put the network interface controllers (NiCs) into promiscuous/monitor mode
  For wired interface, see all network traffic visible on that interface even for unicast data not sent to that NiC
  For wireless interface, see all traffic over the air in the monitor mode

## Slide 12: tcpdump and tcptrace
tcpdump: BSD-license free, packet analyzer program that runs under a command line interface (Source: https://www.tcpdump.org/)
  Display TCP/IP and other packets being transmitted and received over the network
  Use pcap to capture packets
Use libpcap to capture packets
  Can print the content of packets
TCPtrace: free and open-source tool that analyzes the traces from tcpdump (Source: http://www.tcptrace.org/)
May produce different output on each TCP connection
  Elapsed time, bytes and segments sent and received, retransmissions, window advertisements, RTTs and throughput.
As for v5, it also includes minimal UDP processing

## Slide 13: Network simulator ns-3
Discrete event network simulator
  Model the evolution of networked systems through discrete events in time
  Simulation time advances in discrete jumps from event to event
Open source GNU package in C++, with bindings available in Python (Source: https://www.nsnam.org/)
  Simulation programs are C++ executable or Python programs
  Supported for Linux, OS X, and FreeBSD, windows Visual Studio port available
Use libpcap to capture packets
  Can print the content of packets
TCPtrace: free and open-source tool that analyzes the traces from tcpdump
May produce different output on each TCP connection
  Elapsed time, bytes and segments sent and received, retransmissions, window advertisements, RTTs and throughput.
As for v5, it also includes minimal UDP processing

## Slide 14: How ns-3 works?
Packets in discrete events
Full protocol stack
Arbitrary topology you may specify
Supported modules
  Internet, Wi-Fi, LTE, …
  Wired, wireless, …
  Mobility,, static, …

## Slide 15: Ns-3 Model